## Slide 1: IoT Smart Car Psoc X5
Johannes Chopov, Laurence Jorissen, Mohammed Albayyouk

## Slide 2: Project goals
Basis = Remote Controlled car
Data streaming
  Acceleration
  Wheel RPMs
  Distance to obstacles
Collision avoidance
Autonomous driving

## Slide 3: Sensors (inputs)
Distance
  SR-04 Ultrasonic sensors
  Logic level converters
RPM
  Pulse counting module
Acceleration
  MPU6050 (I2C)
Thermistor
  On the PSoC itself.

## Slide 4: Motor components (outputs)
2 - Motor drivers
  Activation pins for each wheel
  Pwm output  rotation speed
4 - DC-motors
2 - 9V batteries
4 - Mecanum wheels

## Slide 5: Distance calculation
SR-04 sends out a pulse
Receives that pulse after a certain amount of time
Time measured using a timer interrupt

## Slide 6: RPM counter
Count #pulses each second
20 holes per full rotation

## Slide 7: Accelerometer
Detect acceleration in X and Z directions.
Neglect Y direction: gravitational accelaration (1g)

## Slide 9: Motor control
Each command corresponds to 8 bits
2 bits/pins per wheel
  Forward (10)
  Backward (01)
  Stationary (00)

## Slide 10: User interface
Controller
Website

## Slide 11: Connection schematic

## Slide 12: FreeRTOS code structure

## Slide 13: Low power mode
PWM signal to limit power drawn by the motor drivers

## Slide 14: Security
Using HiveMQ
Using tls on port 8883
Root CA needed for secure connections

## Slide 15: Links
GitHub:
https://github.com/JohannesChopov/IoT_Project_Group1.git
YouTube:
https://youtu.be/tfyG1CX_znA